INTERNATIONAL CENTRE FOR GENETIC ENGINEERING AND BIOTECHNOLOGY

JNU CAMPUS, ARUNA ASAF ALI MARG,

NEW DELHI 110067

NOTICE INVITING TENDER

Sealed bids are invited from reputed and experienced Chiller manufacturers and HVAC contractors for undertaking the following work. Name of the Work: Supply, Installation, testing and commissioning of Microprocessor controlled, Air cooled Scroll chiller package unit of 60 ± 3 TR capacity  under buy back offer of existing 60 TR Batliboy Make Reciprocating Air Cooled Chillers (Qty 02 Nos)

Schedule of bid submission:

- Date and Time of submission of bid: 27th March, 2020 and 3:00 pm

- Date and time of opening of technical bid: 27th March, 2020 and 4:00 pm

- Date of Financial bid opening: Will be intimated to technically qualified bidders

The tender document can be down loaded from our website  and access the links on to http://www.icgeb.res.in/ndinfo.htm  Interested and eligible contractors are requested to submit the bid complete in all respect along with a tender fee of Rs. 1,500.00 (Non- refundable) and EMD of Rs.34,000/- Bids received without the tender fee and EMD will be summarily rejected.

ICGEB reserves the right of outright rejection of all the bids received without assigning any reason.  The decision of the Institute will be final and binding on all the bidders. In case of cancellation of tender for any reason, the bids will be retained with ICGEB and will not be returned back to the bidders, however EMD will be returned.

Instructions for Bid submission

- Technical bid should contain proof of the following:

- The Bidder should be OEM or his authorized dealer or HVAC contractor. Copies of work order successfully executed for at-least one similar work of not less than Rs 13,60,000/- or Two similar work of not less than Rs. 8,50,000/- each or three works of not less than Rs 6,80,000/-each -in Govt./ PSU/Autonomous bodies, International institutions or Reputed Public Ltd. Company during last seven years

- Satisfactory work completion certificate with contract details. The work order and completion certificate should be for the same work.

(c) Bidder should have its firm/ and or office in Delhi-NCR.

(d) Copies of documents for eligibility criteria (Annexure 1) must be submitted along with Draft of EMD and tender fee in technical bid.

(d) Copy of tender document should be signed and stamped on each page by the authorized signatory

- Financial bid

- Envelop must contain duly filled, signed and stamped financial bid.

The both envelops (Technical and financial bid envelopes) should be super-scribed clearly with Name of work and providing name(s)and postal address of the Bidder with Phone/ Mobile/ Fax numbers and e-mail address if any.

Both “Technical” and “Price” bid should be in separate envelops and then put in to one common envelope, super scribing the Name of the work and NIT No 03/2020 and dropped in the tender box at the reception of ICGEB, New Delhi. Bids received after the schedule time & date will not be entertained or returned

The offer shall remain open for at least 90 days from the date of submission of bids.. Earnest Money Deposit (EMD) amounting to Rs.  Rs.34,000 /- and tender fee of Rs 1,500/- shall be accepted only in the form of Demand Draft drawn in favour of the ICGEB, New Delhi, and payable at New Delhi.

EMD of unsuccessful bidders will be returned after finalization of tender.

EMD is liable to be forfeited if the contractor fails to commence the work as per award letter.

SCOPE OF WORK

- Dismantling and removal of existing 60 TR Batliboy Make Reciprocating Air Cooled Chiller (Qty 02 Nos) and Supply, Installation, testing and commissioning of Microprocessor controlled, Air cooled Scroll chiller 60 ± 3 TR package unit in its place.

- Dismantling and removable of existing GI/ MS chilled water piping, valves, thermal insulation etc. and SITC of new GI/MS pipe , valves thermal insulation etc.

- Provision of instrumentation like PI/TI and water flow switches.

GENERAL TERMS AND CONDITIONS

Name of the Work: Supply, Installation, testing and commissioning of Microprocessor controlled, Air cooled Scroll chiller package unit of 60 ± 3 TR capacity under buy back offer of existing 60 TR Batliboy Make Reciprocating Air Cooled Chiller (Qty 02 Nos)

1) The Work shall be done as per schedule of items, specification terms and conditions and instruction of Engineer-in-charge on as and when required basis.

2) Time limit for completion of work is 60 days from the date of the order issued.

3) The rates shall be inclusive of cartage loading/unloading or any other expenses. GST will be paid as per actual.. Rate must be valid and firm for a period of one year from the date of award of contract/Letter.

4) No Extra charge or any escalation charge will be paid by ICGEB.

5) Inferior and Poor quality material shall not be accepted.

6) The contractor will have to undertake responsibility of accidents etc. for his persons working on site and same will be on stamped paper of Rs.50/100 or the appropriate value (if revised by Govt) The cost of stamp will be borne by the contractor.

7) Before quoting, the contractor must visit the site to inspect the work and shall fully acquaint himself about the conditions and scope of work with regard to accessibility of site required for the satisfactory execution of work. along with site visit certificate. No claim whatsoever shall be entertained by the deptt. on this account.

8) Contractor is to follow relevant Indian standards codes for fire, electricity, safety and building rules.

9) The Contractor shall clean the site after completion of work. Any dismantled material shall be stacked in designated place as instructed by the Engineer-in-charge.

10) Charges for scaffolding or jhula if any, will be considered included in the quoted rates and no extra amount will be paid on this account.

11) Measurement shall be taken jointly by the Engineer-in-Charge or his authorized representative and by the contractor or his authorized representative.

12) All materials brought at site shall be got approved from the Engineer in charge.

13) Contractor shall carry out the various tests as enumerated in CPWD/BIS specification at his own cost.

15) Quantities are indicative and likely to vary. Bidder will have no objection for variation in quantities thereon. Payment will be as per actual work executed.              10% ± deviation in quantities would be permitted.

16) The Director, ICGEB reserves the right to cancel any or all the tenders without assigning any reason.

17) Performance Guarantee @5% shall be deposited to the department on the work order amount by the agency before commencement of work. Performance guaranty shall only be acceptable in the form of bank guarantee /DD/FDR and it will be returned after completion of work.

18) Security deposit of 10 % of final bill amount will be deducted and same will be released after successful expiry of defect liability of 12 months from date of completion of Work. EMD amount of successful bidder will be returned after submission of performance guarantee.

19) Payment terms:

(a)	30% mobilization advance of work order value against bank guarantee of equivalent amount.

(b)	 70% of the work order value against supply of Chiller with accessories. Payment of this will be made after adjusting 30% mobilization advance.

(c)        Balance final payment after completion of the work and submission of the final bill

20)  Security deposit deducted from the final bill will only be released after submission of bank guarantee of CMC

21) In case the bidder resiles from the offer within the validity of tender or contractor fails to work as per specification after issue of the award letter, the earnest money and performance guarantee will be forfeited. Other suitable administrative punitive action may also have imposed as deemed fit.

22) Time allowed for the work shall be strictly followed otherwise the Contractor shall be liable to pay compensation at the rate of 1 % of the contract value of the job undone per week of delay on the part of the Contractor subject to a maximum of 10% of the total contract value.

23) For site visit and any further clarifications, you may visit ICGEB on any working day (Monday to Friday) between 9.30 a.m. to 5 p.m. (contact person Mr. Naresh Chand Dabral and Mr. Joby John).

SPECIAL TERMS AND CONDITION

- PAINTING

All exposed metal work furnished under these specifications, unless otherwise specified, shall be shop and properly painted. Shop coats of paint that have become marred during shipment or erection, shall be cleaned off with mineral spirits, wire brushed and spot painted over the affected areas, then coated with enamel paint to match the finish over the adjoining shop painted surface.

- . TOOLS AND TACKLES

All tools, tackles, supports and staging etc. required for erection and assembly of the equipment and installation covered in the contract shall be provided by the successful bidder himself. In addition, all other materials such as foundation bolts, nuts, etc., required for the installation of the equipment shall also be provided by the successful bidder at his cost.

3	TESTING AND HANDING OVER

i) The contractor shall carry out test run for minimum 15 days from the date of installation in the presence of representatives of ICGEB to establish satisfactory functioning of the installation.

ii) The Installations shall be handed over to ICGEB   after satisfactory testing along with

Two sets of completion documents each consisting of:

a) Detailed equipments data and catalogues.

b) Manufacturer’s maintenance chart including Check chart and Lubrication chart and maintenance manual.

c) Set of “AS INSTALLED DRAWINGS” showing layouts, equipment details, electrical power & control wiring diagrams etc.

d) Test Certificates for major equipments.

iii) Submission of the above documents shall form a pre-condition for the final acceptance of the installation and final payment.

4. SAFETY PRECAUTIONS

i) A competent and authorized Supervisor/Erector shall be on the site whenever the successful bidder’s men are at work. The supervisor/Erector should ensure that all plant and machinery used on the site are rendered safe for working and meets with the Indian or International safety standards applicable for the use and operation of such machinery. The supervisor/erector should also ensure that the workmen at site are made to use safety appliances such as safety belts, life lines, helmets, etc.

ii) It is entirely the responsibility of the successful bidder to practice the principles of ‘SAFETY FIRST’ during the entire tenure of work with adequate insurance covering injury or death of workmen, loss by theft or damage to materials and property and third party.

iii) The successful bidder should clear the site of all debris every day to avoid accidents. In case this is not done, the Owner may engage necessary labour to maintain the cleanliness of the premises and removal of debris and recover all or part of the expenditure so incurred from the successful bidder.

iv) The successful bidder shall, at his own cost, ensure that all of his personnel, employees, workmen and other associated persons working with him at the site are adequately insured as per labour laws and statutory provisions. The successful bidder shall be responsible for all injuries/damages to men, materials and properties etc., which may arise from the operations or negligence of himself and/or his sub-

contractor and indemnify ICGEB for all such expenses, which shall be solely to successful bidder’s own account.’

5. INSURANCE

The successful bidder shall, at his own expense, arrange for insurance policies, such as Workmen Compensation Policy and Bidder’s All Risk Policy in the amount of the Contract effective from the date of commencement of work until final completion, against all of the following risks.

- Injuries and damage of persons, property, animals or things, within or outside the site, arising out of his operations or of any sub-contractors, nominated or otherwise or out of any actions of his employees, agents or representatives.

- Injuries to his or any sub-contractor’s employees.

- Damage to or loss of property, equipment, and materials at site, of the Owner, Bidder and all sub-contractors, as a result of natural causes such as lighting, storm, flood, rain, fire, earthquake, explosion, landslide, etc.

- Damage and injuries to persons, property and materials arising out of riot and civil commotion, theft, sabotage malicious acts, terrorist activities, etc.

- No certificate of payment shall be issued by ICGEB if the Bidder fails to arrange for total insurance cover.

- The bidder shall reinstate in a manner approved by the Project Manager, all damage of every sort entirely at his cost, so as to deliver up to the Owner the whole of the works complete and perfect in all respects and so certified by the Project Manager, ICGEB and also be made good or otherwise satisfy all clause for damage to the property of third parties.

- The bidder shall be responsible for anything within his control and for all risks and consequences, which are not included in the purview of the insurance policies.

- The insurance shall be extended until final completion.

- The bidder undertakes not to cancel any insurance policy or reduce its scope without the written consent of the Project Manager, ICGEB.

- Jurisdiction –

The Contract shall be construed in accordance with and governed in every respect by the laws of India and all actions arising out of or connected with the Contract shall be brought in the Courts of Delhi.

- RECOVERY CLAUSE

- Any damage to building due to negligence of the agency, the same shall be rectified by agency free of cost. Failure to which, the same will be rectified by ICGEB and the amount will be deducted from the agency’s bill.

- Clear the debris from the site is the responsibility of the agency. Failure to which, an amount of Rs 10000/- will be deducted as penalty from the agency’s bill.

- During CMC and Warranty period, the complaint should be attended within a period of 12hrs of complaint lodge. Failure to which, recovery of Rs 1000/- per day per complaint shall be made from the agency’s bill.

- The complaint must be resolved within a period of 72 hrs of complaint lodge. Failure to which a fine of Rs 2000/- per day per complaint will be made from the agency’s bill.

Financial Bid

| S.NO | DESCRIPTION | Make | UNIT | QTY | Rate | Amount |
| --- | --- | --- | --- | --- | --- | --- |
|  | EQUIPEMENTS |  |  |  |  |  |
| 1.0 | AIR COOLED SCROLL CHILLER |  | No | 01 |  |  |
|  | Supply, Installation, testing and commissioning of Microprocessor controlled, Air cooled scroll chillers package unit. Comprising of multiple energy efficient hermetic scroll compressors with direct drive motor, factory insulated with 25 mm PU installation shell and tube type straight tube chiller, fin type air cooled condenser complete with direct driven propeller fans with degree of protection IP-55. The unit should have minimum three compressors,each compressor should have independent refrigerant circuit. The package unit shall be complete with anti vibration mountings, copper refrigerant piping, full charge of refrigerant gas, power and control wiring, safety controls and accessories, expansion valve etc. The compressors shall be suitable for operation on 415 ± 10 % volts, 3 phase, 50 Hz AC power supply. | Blue Star/Daikin/Carrier/York |  |  |  |  |
| a | Cooling capacity: 60 ± 3TR |  |  |  |  |  |
| b | Chilled water leaving temp. : 44 deg. F /6.7 deg.0c |  |  |  |  |  |
| c | Chilled water entering temp. : 54 deg. F /12.2 deg. C |  |  |  |  |  |
| d | Chiller fouling factor: 0.0005 FPS |  |  |  |  |  |
| e | Type of refrigerant: CFC free |  |  |  |  |  |
| f | Power consumption 1.2 KW / TR |  |  |  |  |  |
| 2.0 | CHILLED WATER PUMPS |  | NO | 2 |  |  |
|  | Supply, Installation, Testing and Commissioning of centrifugal pump sets, flow rate of 9.5 LPS for chillers complete with TEFC motor. The pumps shall be suitable for operation on 415 ± 10% volts, 3 phase, 50 Hz AC power supply. | Kirloskar/Becon/Armstrong |  |  |  |  |
| a | Type: Monoblock end suction |  |  |  |  |  |
| b | Body: CI |  |  |  |  |  |
| c | Impeller: Brass /SS |  |  |  |  |  |
| d | Head: 25-30 Mtr |  |  |  |  |  |
| 3.0 | CHILLED WATER PIPING WITH INSULATION |  |  |  |  |  |
|  | Supply, installation,testing and commissioning of C class MS pipe with insulation with necessary fittings (Like elbows, T fittings, flanges etc.) and insulating chilled pipeline using "TF" grade expanded polystyrene molded pipe sections of size 50 mm density not less than 24kg/cu.m after a thick coat of cold setting adhesive (CPRX compound) covered with a layer of 120 grams/sq m polythene sheet (vapour barrier) & finally cladding with 26 gauge Aluminium sheet complete as required. EPS insulation make: Beardsell | JINDAL/ TATA |  |  |  |  |
| a | 65 MM |  | RMT | 24 |  |  |
| b | 50 MM |  | RMT | 12 |  |  |
| 4.0 | Valves & Accessories |  |  |  |  |  |
|  | Supply, Installation, Testing and Commissioning of following necessary valve with flanges and nut and bolts with 50 mm thickness TF quality expanded polystyrene moulded pipe sections of density not less than 24kg/cu.m after a thick coat of cold setting adhesive (CPRX compound) covered with a layer of 120 grams/sq m polythene sheet (vapour barrier) & finally cladding with26 gauge Aluminium sheet complete as required. EPS insulation Make: Beardsell |  |  |  |  |  |
| a | Butterlfy valve 65 MM PN 16 rating ,SS Disc and stem, flanged end connection | Advance/Audco | No | 02 |  |  |
| b | Butterlfy valve 50 MM PN 16 rating ,SS SS Disc and stem, flanged end connection | Advance/Audco | No | 04 |  |  |
| c | Balancing Valve 65 MM PN 16 rating ,SS SS Disc and stem, flanged end connection | Advance/Audco | No | 01 |  |  |
| d | NRV 50 MM | Advance/Audco | No | 02 |  |  |
| e | Y Strainer – 65 MM | Rapid cool/Emrald | No | 01 |  |  |
| f | Y Strainer – 50 MM | Zoloto/Emrald | No | 02 |  |  |
| g | Pressure Gauge 6” Dial, Range 0-10 kg/sqcm,bottom connection 3/8” BSPT, brass bourdon tube with Extra Long M.S. Threaded Socket (heavy) welded on MS pipe, SS Nipple, SS Ball Valve (Shenco - make), SS U-tube (Sch 40), SS Socket (heavy) etc., of the following: Range: 0-10 kg/cm2 | H Guru/Waree | No | 06 |  |  |
| h | Dial type SS Temperature Indicator, 6” dia., 0-60 Deg C,Bimetal / Rigid stem type. | H Guru/Waree | No | 02 |  |  |
| 5.0 | water flow switch with control wiring | Danfoss/ Rapid Control/Anergy/ Emerald/ Johnsons Control Honeywell | No | 01 |  |  |
| 6.0 | Termination of old cables, earhting to New chiller & pumps. |  | SET | 1 |  |  |
| 7.0 | Supply, Installation, Testing and Commissioning of 9 KW Pan Humidifier with valves and piping complete as required | Rapid cool /Sant | No | 03 |  |  |
| 8.0 | CMC Cost of the chiller for 5 years after completion of warranty period |  |  |  |  |  |
|  | 1st year |  |  |  |  |  |
|  | II ndyear |  |  |  |  |  |
|  | III rd year |  |  |  |  |  |
|  | IV th year |  |  |  |  |  |
|  | Vth year |  |  |  |  |  |
| 9.0 | Buy back discount offered by bidder for Old 60TR chillers |  | SET | 2 |  |  |
| 10 | Total Rs (Sl. No. 1+2+3+4+5+6+7+8 -9) |  |  |  |  |  |

Note:         1.	Above prices should be without GST.      2. GST will be paid as per actual

- CMC shall be provided by OEM/ Authorised Channel partner.

Annexure I

PERFORMA FOR ELIGIBILITY CRITERIA

1 Name of the Agency:

2. Office Address and Tel. Nos. Email ID:

3.Registration details (with documentary evidence)

4. PAN No. (with documentary evidence)

5. Annual turnover for last three years ending March 2019 supported with documentary evidence.

6. Experience (last seven years) ending March 2019 (copies of work orders and completion certificates if fully executed)

7. Signed and stamped Tender document

8. Tender Fee

9. Earnest Money Deposit

10. Signed and stamped Site visit acceptance certificate                                  (Attached as annexure II)

11. Bidder should have its firm or office in Delhi –NCR.

12. Equipment Commissioning shall be done by OEM/ Channel Partner

13. Bank Details

Annexure II

CERTIIFACTE FOR SITE INSPECTION

Certified that we have visited the site on _________________and assessed the nature and amount of work involved before submitting our offer. We will be able to complete the works within the stipulated time and also we will be able to execute the work suit the site condition.

(Signature of Bidder with Seal)

Name:

Address:

Date:

Component In Charge

ICGEB