INTERNATIONAL CENTRE FOR GENETIC ENGINEERING AND BIOTECHNOLOGY

JNU CAMPUS, ARUNA ASAF ALI MARG,

NEW DELHI 110067

NOTICE INVITING TENDER

Sealed bids are invited from reputed and experienced contractors for undertaking the following work. Name of the Work: Construction of Lab space in the basement of New building at ICGEB

Schedule of bid submission:

- Pre Bid meeting: 30th October, 2019 at 3:00 PM

- Date of bid submission and time: 14th November, 2019 and 3:00 PM

- Date of technical bid opening and time: 14th November, 2019 and 4:00 PM

- Date of Financial bid opening: Will be intimated to technically qualified bidders

The Scope of work and the tender document are appended below can be down loaded from our website  and access the links on to http://www.icgeb.res.in/ndinfo.htm  Interested and eligible contractors are requested to submit the bid complete in all respect along with a tender fee of Rs1,000.00 (Non- refundable) and EMD of Rs.26,000 /- Bids received without the tender fee and EMD will be summarily rejected.

ICGEB reserves the right of outright rejection of all the bids received without assigning any reason.  The decision of the Institute will be final and binding on all the bidders. In case of cancellation of tender for any reason, the bids will be retained with ICGEB and will not be returned back to the bidders, however EMD will be returned.

Instructions for Bid submission

- Technical bid should contain proof of the following:

- The Bidder should be Reputed contractor and must have executed at-least one similar work of Rs 10,40,000/- or Two similar work of Rs. 6,50,000/- each or 03 works of Rs 5,20,000/-each -in Govt./ PSU/Autonomous bodies, International institutions or Reputed private sector.

(b) Bidder should have its firm/ and or office in Delhi-NCR.

(c) Copies of documents for eligibility criteria (Annexure 1) must be submitted along with Draft of EMD and tender fee in technical bid.

(d) Copy of tender document should be signed and stamped on each page by the authorized signatory

- Financial bid

- Envelop must contain duly filled, signed and stamped financial bid.

The both envelops (Technical and financial bid envelopes) should be super-scribed clearly with Name of work and providing name(s)and postal address of the Bidder with Phone/ Mobile/ Fax numbers and e-mail address if any.

Both “Technical” and “Price” bid should be in separate envelops and then put in to one common envelope, super scribing the Name of the work and NIT No 07/2019 and dropped in the tender box at the reception of ICGEB, New Delhi. Bids received after the schedule time & date will not be entertained or returned

The offer shall remain open for at least 60 days. Earnest Money Deposit (EMD) amounting to Rs26,000 /- and tender fee of Rs 1000/- shall be accepted only in the form of Demand Draft drawn in favour of the ICGEB, New Delhi, and payable at New Delhi. EMD and tender fee must be enclosed with technical bid failing which, bid will summarily be rejected.

EMD of unsuccessful bidders will be returned after finalization of tender. EMD is liable to be forfeited if the contractor fails to commence the work as per award letter.

SCOPE OF WORK

| BOQ for Proposed Laboratory |
| --- |
| S.No. | Description | Unit | Quantity |
| 1 | Al. Partitions, and Related Works |  |  |
|  | Providing/fabricating/assembling and fixing Anodized aluminium Fixed partition medium (16 gauge) Weight aluminium section as follows.) Horizontal members Size - 63.50 x 38.10 mm Top portion 5mm thick plain glass (Modi Make) with all necessary fittings/fixtures etc., complete. at0.75 kg/member. Novo pan pre laminated board 12mm Size: - 63.50 x 38.10mm The work including necessary clips, rubber beading aluminium triangular beading, complete and fixing to the adjoining members wall/frame work with all necessary fittings/ fixture etc., complete | sft | 650 |
| 2 | DOOR SYSTEM |  |  |
|  | Providing/fabricating/assembling and fixing Anodized aluminium Door (16 gauge) with medium Weight aluminium section as follows.) Horizontal members Size - 63.50 x 38.10 mm Top portion 5mm thick plain (Modi Make) glass with all necessary fittings/fixtures etc., complete. at0.75 kg/member. Novo pan pre laminated board 12mm Size: - 63.50 x 38.10mm The work including necessary clips, rubber beading aluminium triangular beading, lOCK , HINGES. DOOR CLOSER. HANDLE complete with all necessary fittings/ fixture etc., complete |  |  |
| a | HINGES DOOR | NOS | 1 |
| b | SLIDING DOOR | NOS | 2 |
| 3 | GYPSUM BORAD PARTITION. |  |  |
|  | Providing and fixing GYPSUM partition upto ceiling height consisting of G.I. frame and required board, including providing and fixing of frame work made of special section power pressed/ roll form G.I. sheet with zinc coating of 120 gms/sqm(both side inclusive), consisting of floor and ceiling channel 50mm wide having equal flanges of 32 mm and 0.50 mm thick, fixed to the floor and ceiling at the spacing of 610 mm centre to centre with dash fastener of 12.5 mm dia meter 50 mm length or suitable anchor fastener or metal screws with nylon plugs and the studs 48 mm wide having one flange of 34 mm and other flange 36 mm and 0.50 mm thick fixed vertically within flanges of floor and ceiling channel and placed at a spacing of 610 mm centre to centre by 6 mm dia bolts and nuts, including fixing of studs along both ends of partition fixed flush to wall with suitable anchor fastener or metal screws with nylon plugs at spacing of 450 mm centre to centre, and fixing of boards to both side of frame work by 25 mm long dry wall screws on studs, floor and ceiling channels at the spacing of 300 mm centre to centre. COMPLETE WITH GLASS WOOL IN FILLED MATERIAL AND ACRYLIC EMULSION PAINT ON WALL | SFT | 375 |
| 4 | False Ceiling Work |  |  |
|  | Removing and reinstallation of existing corridor gypsum False Ceiling which will be damaged during the said work | SFT | 100 |
| 5 | Providing and Fixing 2 TR Split Air Conditioning Unit (Inverter type WITH ONLY COOLING with only copper coil.) complete with fixing of both indoor and outdoor unit and copper piping (Minimum 20 RMT) for refrigerant and PVC piping for condensate etc. The unit will be of 3-star BEE rating which will be included in the cost. -Inverter model, Daikin /, Hitachi WITH mild steel frame for supporting of outdoor unit . | each | 2.00 |
| 6 | Electrical Work (ELECTRICAL power point UPS/RAW) |  |  |
| a | Supply and fixing of modular type single phase 1nos 16A 5pin Socket with front plate/ 2 nos 16 A 5 pin socket with front plate .( Havells,) | Nos. | 50 |
| b | Supply and fixing of 1-PHASE with 32A DP MCB in MS box including all fixing accessories. ( Havells,) | Nos. | 2 |
| c | Al. Box Channel for running and fixing of Socket on Partition wall | Rmt | 50 |
| d | Supply and fixing of factory made 3-phase 63 A TPN MCB with MS box including all fixing accessories. Havells make | Nos. | 3 |
| e | 2runs of 4Sq.mm wires with 1run of 2.5 Sq.mm wire in 25 mm dia conduit (For 6A/16A Sockets) ( Havells, Finolex) | RM | 200 |
| f | 2 runs of 6 Sq.mm wires with 1 run of 4 Sq.mm wire in 25 mm dia conduit. (32 A DP MCB)( Havells, Finolex) | RM | 150 |
| g | 4 runs of 10 Sq.mm wires with 2 run of 6 Sq.mm wire in 32 mm dia conduit. (63 A TPN)( Havells, Finolex) | RM | 150 |
| 7 | Conduit for Electrical Wiring |  |  |
| a | 25mm dia pvc conduit | RM | 500 |
| b | 32mm dia pvc conduit | RM | 100 |
| 8 | Cables, Mains and Submains/ Thimbals as required |  |  |
| a | 4 c x 16 sq.mm XLPE AL. AR CABLE ( Havells, Finolex) | RM | 70 |
| b | 4 c x 16 sq.mm XLPE CU. AR CABLE ( Havells, Finolex)( Havells, Finolex) | RM | 70 |
| c | 6sq mm 4 core wire for AHU wiring (Flexible Copper) ( Havells, Finolex) | RM | 70 |
| d | 10sq mm 4 core wire for out wiring (Flexible Copper) ( Havells, Finolex) | RM | 80 |
| 9 | Distribution Boards |  |  |
|  | Design, manufacture, supplying, installing, testing and commissioning of the following cubical type 2mm thick sheet steel enclosed fully recessed type, TPN Miniature Circuit Breakers Distribution Boards dust proof, vermin proof, with hinged and lockable doors complete with DP MCB Isolators and inter-connection with copper wires, or copper tapes, cable glands/conduit entry bushes, bonding to earth and painting. Also provide separate neutral busbar for each phase. Provide separate Earth Links. Use brass thimbles for connections of all wires. Supply and installation of sheet metal enclosed double door 12 way TPN DB, each phase consisting of 12 Nos. 10/20 AMP SP MCB’s and controlled by one number 30 mA sensitivity 63 AMPS DP ELCB in each phase backed up with 1 No 100 Amps 4P MCB as a main incomer. (All MCBs are Havells, schenider and L&T) |  |  |
| a | 12 way DB ( Havells / schenider ) | Nos.. | 1.00 |
| b | 8 way DB( Havells / schenider ) | Nos.. | rate only |
| 10 | Exhaust ducting for Laboratory equipment complete with fan and flexible ducting | set | 1 |
| 11 | Re Installation of Existing AHU and Testing / Commissioning Treated fresh Unit. Re Installation of 7.5 TR condensing unit for Treated Fresh Unit complete with all accessories. Inter connecting Copper piping , for Refrigerant with Minor Civil Work and Ms stand for foundation. | Nos | 1 |
| 12 | Supply and installation of water pipe line of C-PVC of 20mm size with all accessories and connection complete with TEE Band, Elbow and etc. Astral/ Ashirwad Make | Rmt | 150 |
| 13 | Supply, Installation & Testing of sheet metal Ducting as per SMACNA , vanes, splitters, duct supports gaskets for joints etc. GI Sheet Metal Ducting (Rectangular) joints and pressure tested etc as per SMACNA and specifications. 24 SWG Duct for Fresh air. | Sq, M | 150 |
| 14 | Supply and Installation of supply Damper for Fresh air Unit. | Nos | 1 |
| 15 | Supply and Installation of Canvas | Nos | 1 |
| 16 | Supply and Installation of Grill for supply air. | SQMT | 3 |
| 17 | Supply and Installation of 13 MM Foam Insulation for Fresh air Duct. | Sq. M | 150 |
| 18 | Supply and Installation of one No AHU Electrical panel with al accessories for supply of power to control AHU and Condensing Unit. | 1 | no |

GENERAL TERMS AND CONDITIONS

Name of the Work: Construction of Lab space in the basement of New building at ICGEB

1) The Work shall be done as per schedule of items, specification terms and conditions and instruction of Engineer-in-charge on as and when required basis.

2) Time limit 45 days from the date of the order issued.

3) The rates shall be inclusive of cartage/ loading unloading or any other expenses. GST should be clearly shown separately. Rate must be valid and firm for a period of one year from the date of award of contract/Letter.

4) No Extra charge or any escalation charge will be paid by ICGEB.

5) Inferior and Poor quality material will be rejected and work order may be cancelled.

6) The contractor will have to undertake responsibility of accidents etc. for his persons working on site and same will be on stamped paper of Rs.50/100 or the appropriate value (if revised by Govt) The cost of stamp will be borne by the contractor.

7) Before quoting, the contractor is advised to inspect the site of work and shall fully acquaint himself about the conditions and scope of work with regard to accessibility of site required for the satisfactory execution of work. No claim whatsoever shall be entertained by the deptt. on this account.

8) Contractor is to follow relevant Indian standards codes for fire, electricity, safety and building rules.

9) The Contractor shall clean the site after completion of work . Any dismantled material shall be stacked in designated place as instructed by the Engineer-in-charge.

10) Charges for scaffolding or jhula if any, will be considered included in the quoted rates and no extra amount will be paid on this account.

11) Measurement shall be taken jointly by the Engineer-in-Charge or his authorized representative and by the contractor or his authorized representative.

12) All materials brought at site shall be got approved from the Engineer-in-charge before being used. The Contractor shall, at his expense and without delay supply for approval to engineer-in-charge, samples of each material such as square bar, flat bar, MS flat & MS Tee, MS angle and other items along with test certificate as desired.

13) Contractor shall carry out the various tests as enumerated in CPWD/BIS specification at his own cost.

14) The welding, if involved, must be thoroughly joined & beads; kinks should not be visible. The jointing flux material should be uniformly spread to achieve desired strength. Grinder shall be used to remove bulged out metallic flux.

15) No sub-Contracting or sub-letting is allowed.

16) Quantities shown in the schedule are tentative and may change as per site conditions.

17) 10% ± deviation in quantities would be permitted for required items as per instruction of Component I/C.

18) Quantities are indicative and likely to vary. Bidder will have no objection for variation in quantities thereon. Payment will be as per actual work executed.

19) The lowest bidder will be awarded order for work.

20) The Director, ICGEB reserves the right to cancel any or all the tenders without assigning any reason.

21) No escalation in any form either of materials or of labour shall be payable by the Centre.

22) No T & P and scaffolding shall be supplied by the Institute.

23) No advance payment shall be made except if specified otherwise in the tender.

24) Performance Guarantee @5% shall be deposited to the department on the tendered amount by the agency before commencement of work. Performance guaranty shall only be acceptable in the form of bank guarantee /DD.

25) Security deposit of 5% of final bill amount will be deducted and same will be released after successful expiry of defect liability of 12 months from date of completion of Work. EMD amount of successful bidder will be returned after submission of performance guarantee.

26) EMD of unsuccessful bidders will be returned after finalization of tender.

27) EMD is liable to be forfeited if the contractor fails to commence the work as per award letter.

28) For proper completion of the work, if any quantity variation or extra items are required, the bidder shall execute the same. Rates of extra items shall be derived from the tender itself as far as possible or else prevailing market rates shall be adopted.

29) In case the bidder resiles from the offer within the validity of tender or contractor fails to work as per specification after issue of the award letter, the earnest money will be forfeited. Other suitable administrative punitive action may also have imposed as deemed fit.

30) Time allowed for the work shall be strictly followed otherwise the Contractor shall be liable to pay compensation at the rate of 1 % of the contract value of the job undone per week of delay on the part of the Contractor subject to a maximum of 10% of the total contract value.

31) For site visit and any further clarifications, you may visit ICGEB on any working day (Monday to Friday) between 9.30 a.m. to 5 p.m. (contact person Mr. Naresh Chand Dabral and Mr. Joby John).

32). Payment terms: No advance is permissible under normal circumstance. Bill of the full work may be submitted after satisfactory installation & completion of work (within 15 days of completion).

However, for any reason beyond the control of the Contractor the extension of time shall be granted upon application by the Contractor in prescribed format. No claim for any compensation during the extended period shall be entertained and the ICGEB’s decision in this regard shall be final.

| FINANCIAL BID |  |  |
| --- | --- | --- |
| S.No. | Description | Unit | Quantity | RATE | AMOUNT |
| 1 | Al. Partitions, and Related Works |  |  |  |  |
|  | Providing/fabricating/assembling and fixing Anodized aluminium Fixed partition medium (16 gauge) Weight aluminium section as follows .) Horizontal members Size - 63.50 x 38.10 mm Top portion 5mm thick plain glass (Modi Make) with all necessary fittings/fixtures etc., complete. at0.75 kg/member. Novopan pre laminated board 12mm Size: - 63.50 x 38.10mm The work including necessary clips, rubber beading aluminium triangular beading, complete and fixing to the adjoining members wall/frame work with all necessary fittings/ fixture etc., complete | sft | 650 |  |  |
| 2 | DOOR SYSTEM |  |  |  |  |
|  | Providing/fabricating/assembling and fixing Anodized aluminium Door (16 gauge) with medium Weight aluminium section as follows.) Horizontal members Size - 63.50 x 38.10 mm Top portion 5mm thick plain (Modi Make) glass with all necessary fittings/fixtures etc., complete. at0.75 kg/member. Novopan pre laminated board 12mm Size: - 63.50 x 38.10mm The work including necessary clips, rubber beading aluminium triangular beading, lOCK , HINGE. DOOR CLOSER. HANDLE complete with all necessary fittings/ fixture etc., complete |  |  |  |  |
| a | HINGE DOOR | NOS | 1 |  |  |
| b | SLIDING DOOR | NOS | 2 |  |  |
| 3 | GYPSUM BORAD PARTITION. |  |  |  |  |
|  | Providing and fixing GYPSUM partition upto ceiling height consisting of G.I. frame and required board, including providing and fixing of frame work made of special section power pressed/ roll form G.I. sheet with zinc coating of 120 gms/sqm(both side inclusive), consisting of floor and ceiling channel 50mm wide having equal flanges of 32 mm and 0.50 mm thick, fixed to the floor and ceiling at the spacing of 610 mm centre to centre with dash fastener of 12.5 mm dia meter 50 mm length or suitable anchor fastener or metal screws with nylon plugs and the studs 48 mm wide having one flange of 34 mm and other flange 36 mm and 0.50 mm thick fixed vertically within flanges of floor and ceiling channel and placed at a spacing of 610 mm centre to centre by 6 mm dia bolts and nuts, including fixing of studs along both ends of partition fixed flush to wall with suitable anchor fastener or metal screws with nylon plugs at spacing of 450 mm centre to centre, and fixing of boards to both side of frame work by 25 mm long dry wall screws on studs, floor and ceiling channels at the spacing of 300 mm centre to centre. COMPLETE WITH GLASS WOOL IN FILLED MATERIAL AND ACRYLIC EMULSION PAINT ON WALL | SFT | 375 |  |  |
| 4 | False Ceiling Work |  |  |  |  |
|  | Removing and reinstallation of existing corridor gypsum False Ceiling which will be damaged during the said work | SFT | 100 |  |  |
| 5 | Providing and Fixing 2 TR Split Air Conditioning Unit (Inverter type WITH ONLY COOLING with only copper coil. ) complete with fixing of both indoor and outdoor unit and copper piping ( Minimum 20 RMT) for refrigerant and PVC piping for condensate etc. The unit will be of 3-star BEE rating which will be included in the cost. -Inverter model, Daikin /, Hitachi WITH mild steel frame for supporting of outdoor unit . | each | 2.00 |  |  |
| 6 | Electrical Work (ELECTRICAL power point UPS/RAW) |  |  |  |  |
| a | Supply and fixing of modular type single phase 1nos 16A 5pin Socket with front plate/ 2 nos 16 A 5 pin socket with front plate .( Havells,) | Nos. | 50 |  |  |
| b | Supply and fixing of 1-PHASE with 32A DP MCB in MS box including all fixing accessories. ( Havells,) | Nos. | 2 |  |  |
| c | Al. Box Channel for running and fixing of Socket on Partition wall | Rmt | 50 |  |  |
| d | Supply and fixing of factory made 3-phase 63 A TPN MCB with MS box including all fixing accessories. Havells make | Nos. | 3 |  |  |
| e | 2runs of 4Sq.mm wires with 1run of 2.5 Sq.mm wire in 25 mm dia conduit (For 6A/16A Sockets) ( Havells, Finolex) | RM | 200 |  |  |
| f | 2 runs of 6 Sq.mm wires with 1 run of 4 Sq.mm wire in 25 mm dia conduit. (32 A DP MCB)( Havells, Finolex) | RM | 150 |  |  |
| g | 4 runs of 10 Sq.mm wires with 2 run of 6 Sq.mm wire in 32 mm dia conduit. (63 A TPN)( Havells, Finolex) | RM | 150 |  |  |
| 7 | Conduit for Electrical Wiring |  |  |  |  |
| a | 25mm dia pvc conduit | RM | 500 |  |  |
| b | 32mm dia pvc conduit | RM | 100 |  |  |
| 8 | Cables, Mains and Submains/ Thimbals as required |  |  |  |  |
| a | 4 c x 16 sq.mm XLPE AL. AR CABLE ( Havells, Finolex) | RM | 70 |  |  |
| b | 4 c x 16 sq.mm XLPE CU. AR CABLE ( Havells, Finolex)( Havells, Finolex) | RM | 70 |  |  |
| c | 6sq mm 4 core wire for AHU wiring (Flexible Copper) ( Havells, Finolex) | RM | 70 |  |  |
| d | 10sq mm 4 core wire for out wiring (Flexible Copper) ( Havells, Finolex) | RM | 80 |  |  |
| 9 | Distribution Boards |  |  |  |  |
|  | Design, manufacture, supplying, installing, testing and commissioning of the following cubical type 2mm thick sheet steel enclosed fully recessed type, TPN Miniature Circuit Breakers Distribution Boards dust proof, vermin proof, with hinged and lockable doors complete with DP MCB Isolators and inter-connection with copper wires, or copper tapes, cable glands/conduit entry bushes, bonding to earth and painting. Also provide separate neutral bus bar for each phase. Provide separate Earth Links. Use brass thimbles for connections of all wires. Supply and installation of sheet metal enclosed double door 12 way TPN DB, each phase consisting of 12 Nos. 10/20 AMP SP MCB’s and controlled by one number 30 mA sensitivity 63 AMPS DP ELCB in each phase backed up with 1 No 100 Amps 4P MCB as a main incomer. (All MCBs are Havells, schenider and L&T) |  |  |  |  |
| a | 12 way DB ( Havells / schenider ) | Nos.. | 1.00 |  |  |
| b | 8 way DB( Havells / schenider ) | Nos.. | rate only |  |  |
| 10 | Exhaust ducting for Laboratory equipment complete with fan and flexible ducting | set | 1 |  |  |
| 11 | Re Installation of Existing AHU and Testing / Commissioning Treated Fresh Unit. Re Installation of 7.5 TR condensing unit for Treated Fresh Unit complete with all accessories. Inter connecting Copper piping , for Refrigerant with Minor Civil Work and Ms stand for foundation. | Nos | 1 |  |  |
| 12 | Supply and installation of water pipe line of C-PVC of 20mm size with all accessories and connection complete with TEE Band, Elbow and etc. Astral/ Ashirwad Make | Rmt | 150 |  |  |
| 13 | Supply, Installation & Testing of sheet metal Ducting as per SMACNA , vanes, splitters,duct supports gaskets for joints etc. GI Sheet Metal Ducting (Rectangular) joints and pressure tested etc as per SMACNA and specifications. 24 SWG Duct for Fresh air. | Sq, M | 150 |  |  |
| 14 | Supply and Installation of supply Damper for Fresh air Unit. | Nos | 1 |  |  |
| 15 | Supply and Installation of Canvas | Nos | 1 |  |  |
| 16 | Supply and Installation of Grill for supply air. | SQMT | 3 |  |  |
| 17 | Supply and Installation of 13 MM Foam Insulation for Fresh air Duct. | Sq. M | 150 |  |  |
| 18 | Supply and Installation of one No AHU Electrical panel with al accessories for supply of power to control AHU and Condensing Unit. | 1 | no |  |  |
|  | TOTAL |  |  |  |  |

Annexure I

Performa for eligibility criteria

1 Name of the Agency:

2. Office Address and Tel. Nos. Email ID:

3.Registration details (with documentary evidence)

4. PAN No. (with documentary evidence)

5. Annual turnover for last three years supported with documentary evidence.

6. Experience (last three years) (copies of work orders and completion certificates if fully executed)

7. Signed and stamped Tender document

8. Tender Fee

9. Earnest Money Deposit

10. Site visit acceptance certificate (signed and stamped)

Annexure II

CERTIIFACTE FOR SITE INSPECTION

Certified that we have visited the site on _________________and assessed the nature and amount of work involved before submitting our offer. We will be able to complete the works within the stipulated time and also we will be able to execute the work suit the site condition.

(Signature of Bidder with Seal)

Name:

Address:

Date:

Component In Charge

ICGEB